Ruleblock for Obstacles Avoidance and turn_speed

obs_angle --> / obs_distance | \/	far_left	left	center	right	far_right
close	right	fast_right	fast_right	fast_left	Left
medium	center	Right	Right	Left	center
far	center	center	center	center	center

Ruleblock for Obstacles Avoidance and velocity turn_speed

obs_angle --> / obs_distance | \/	far_left	left	center	right	far_right
close	Medium	Slow	Slow	Slow	Medium
medium	Fast	Medium	Slow	Medium	Fast
far	Fast	Fast	Fast	Fast	Fast

Ruleblock for Target Steering

Target_angle --> / Target _distance | \/	left	center	right
finish	turn_speed = fast_right velocity = stop	turn_speed = center velocity = stop	turn_speed = fast_left velocity = stop
close	turn_speed = fast_right velocity = slow	turn_speed = center velocity = slow	turn_speed = fast_left velocity = slow
medium	turn_speed = right velocity = medium	turn_speed = center velocity = slow	turn_speed = left velocity = medium
far	turn_speed = right velocity = fast	turn_speed = center velocity = fast	turn_speed = left velocity = fast